## Slide 1
Requirements on EIC detector tracking system
Alexander Kiselev
EIC Tracking R&D Workshop at Temple University
May,9 2015

## Slide 2: Acceptance: electrons
Q2 > 1.0 GeV2: rapidity coverage -4 < h < 1 is sufficient
Q2 < 0.1 GeV2: a dedicated low-Q2 tagger is required
Increasing lepton beam energy: scattered lepton is boosted to negative h
{PYTHIA events at different electron energy}

## Slide 3: Acceptance: hadrons
Increasing lepton beam energy boosts hadrons more to negative pseudorapidity
Increasing hadron beam energy influences max. hadron energy at fixed pseudorapidity
(and p±, K±, p± look
the same)
range -3<h<3 covers entire pt & z region important for physics
{same set of PYTHIA events; Q2>1 GeV2, 0.01<y<0.95, z>0.1 cuts applied}

## Slide 4: Configuration: whole detector
hadronic calorimeters
TPC
e/m calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid coils
-4<h<4: Tracking & e/m Calorimetry (hermetic coverage)

## Slide 5: Configuration: tracker
TPC
silicon trackers
GEM trackers
3T solenoid coils
ALICE
SBS

## Slide 6: Material budget
On the ~5% X/X0 level pretty much in the whole acceptance
“Core” part only (no TPC outer field cage & endcaps; no GEMs)

## Slide 7: “Raw” momentum resolution
High resolution up to (at least) |h|~3
p+
{Box generator at fixed momentum and pseudorapidity}

## Slide 8: Smearing in kinematic variables
{PYTHIA 20x250 GeV, NO bremsstrahlung} -> {GEANT} -> {Kalman filter track fit}
same procedure; simulation WITH bremsstrahlung
-> looks good despite poor resolution at low Y and long bremsstrahlung tails

## Slide 9: “Purity” in (x,Q2) kinematic bins
Describes migration between kinematic bins
Important to keep it close to 1.0 for successful unfolding
bremsstrahlung OFF
bremsstrahlung ON
Bremsstrahlung matters even for detector with ~5% X/X0
“Straightforward” tracking can hardly help at Y<0.1

## Slide 10: R&D topics: MAPS
p+; h=3
Reduce further material budget
Minimize integration time
Minimize dead area material
Optimize cooling system
Develop forward disk setup
Basically need to adapt ALICE design to the EIC environment
pixel size effect

## Slide 11: R&D topics: TPC
Attain ILD design single point resolution level
Minimize ion back flow
Establish operation in highly inhomogeneous magnetic field
Establish acceptable dE/dx performance with GEM readout
Improve shaper timing
Reduce inner field cage material budget …
… same for the endplate
Attain higher drift velocities (?)
RICH-mode operation (?)
Need a high resolution medium size TPC

## Slide 12: R&D topics: GEMs
Establish high resolution at large track slopes
Deliver reliable “vector” measurement
Minimize material budget (?)
Develop large-scale GEMs
Be able to cover close-to-beam-line area
Need high resolution medium size GEMs
With-GEM vs no-GEM momentum resolution
NB: 50 micron spatial resolution assumed!

## Slide 13: R&D topics: MicroMegas
EIC R&D
(Temple, Saclay)
Establish <100 micron spatial resolution in a 3T field
Deliver reliable “vector” measurement
Develop large scale samples
Minimize material budget
Track finding may benefit greatly from fast devices providing “vector” track seeds

## Slide 14: Costs

## Slide 15: Auxiliary acceptance detectors
electrons
Legend:
beam pipe
hadron magnet apertures
electron magnet apertures
0 m
-4.5 m
+4.5 m
-15 m
-31 m
-33m
-45 m
+18 m
Roman Pots
low Q2 tagger
photon transport line with Al exit window
dipole magnet for pair spectrometer
emcals for lumi monitor

## Slide 16: Other considerations
Vertex resolution: with MAPS we get it better than 10 microns
Radiation hardness: not a problem?
Readout speed and FE -> main DAQ throughput: acceptable?